## Slide 1: Window Frost Detector
Wouter Huygen, Tom Raeves, Tijs van Alphen and Matthias Wuyts

## Slide 2: Block Diagram Overview
Logic
BLE
LoRa
App
Device
Mobile Phone
UART
Backend
FDService
API
TTN Cloud
FCM
Notes: The main idea we had was to get a notification if our car window is frosted. The octa does some measurements using the temperature/humidity sensor. This data gets send from the device to The Things Network cloud over LoRaWan. From the ttn cloud it gets send to the backend server using MQTT (Message Queuing Telemetry Transport), a lightweight publish-subscribe networkprotocol that uses TCP-UDP. This way the application can get the data using a HTPP GET request. Everytime a new reading comes in on the backend, a notification gets send to the application using FireBase Cloud messaging. We also use BLE to send the alarm we set in the application to the device.

## Slide 3: BLE - Chip

## Slide 4: Goal
Communication smartphone OCTA
  Send the new alarm time to the BLE chip
    Sending a variable through Bluetooth to BLE chip (alarm time)
  Send the alarm time to the OCTA through UART
OCTA
UART

## Slide 5: Problems
Custom Service
  Different SDK versions (different libraries)
  Different functionalities working in different SDK’s
UART
  Enabling UART and a lot of defines, includes and Makefile libraries
  Different nRF-Connect apps for apple and android (with different functions)
  Hard to debug
Coupling BLE and custom app

## Slide 6: Achieved
Connection established
Notes: NUS = Nordic UART service

## Slide 7: OCTA - LoRaWAN

## Slide 8: Goal
Communication OCTA Back end
  Measuring data (Humidity, Temperature and Battery level)
  Packaging our measurements in a LoRaWAN message
  Send our LoRaWAN message

## Slide 9: Problems
Receiving UART messages
  Timing of receiving messages
  Datatype unclarity of UART messages
Watchdog timer
  Resets OCTA in sleep mode
Wake up sleeping OCTA

## Slide 10: Achieved
Messages composed and sent successfully

## Slide 11: RTC Alarm (failed to implement)

## Slide 12: Goal
Receive alarm interrupt to wake up from low power mode
Alarm is set by app
RTC keeps running while in low power mode
Set current time and alarm with data from BLE message
WAKE UP!

## Slide 13: Train of thought
Set up interrupts
1
Set the current time
2
Set the alarm
3
Set correct IRQ_Handler (failed)
4

## Slide 14: Problems
Time and alarm already set in RTC_init()
  Fix: Alarm can be edited (unlock rtc)
WWDG IRQ handler does not find correct IRQ handler
  Gets stuck in infinite loop
Notes: The first problem I encountered was that I could not set the time or alarm, as it was already set in RTC_Init(). After some research I discovered that the real time clock was locked. Easy fix: unlock rtc. Another problem was with the interrupts. I spent a lot of time trying to figure it out why the WWDG IRQ handler got stuck in an infinite loop, but could not find a solution. In the end, I decided to spend my time on trying to get sleepmode to work.

## Slide 15: Achieved (but not implemented)
Set Time
Set Alarm
Notes: Unfortunately I could not implement this in time. It worked on my local project, but I had some troubles with the interrupts. They didn’t come through. However the alarm and time was set correctly as I could print them out in a terminal.

## Slide 16: Low Power Mode

## Slide 17: Goal
After sending and receiving data go to sleep
  Low power usage
  Keep clock running for RTC alarm
Get out of sleep mode
  On interrupt from RTC alarm
  On press of button from octa

## Slide 18: Problem
IRQ handler already defined
  Fix:
Failed for RTC alarm interrupt
  USE_HAL_RTC_REGISTER_CALLBACKS = 0
  Changing value did not work
  Define value in make file did not work

## Slide 19: Achieved
Go to sleep
Notes: disable the systick interrupt first, or else this interrupt will wake the MCU from Low Power mode after 1ms.
Another possible option is to go to standby mode or STOP mode instead of sleep mode.
In sleep mode CPU CLK is turned OFF and there is no effect on other clocks or analog clock sources. The current consumption is HIGHEST in this mode, compared to other Low Power Modes.
In stop mode all clocks in the 1.8V domain are stopped, the PLL, the HSI and the HSE oscillators are
disabled. SRAM and register contents are preserved. In the stop mode, all I/O pins keep the same state as in the run mode.
In standby mode the 1.2 V domain is consequently powered off. Voltage regulator is disabled. 1.8-1.2V domain is powered OFF. SRAM & register contents are lost except registers in the standby circuit.

## Slide 20: Power Profiling

## Slide 21: Power Profiling: Active (reading + LoRaWAN msg)

## Slide 22: Power Profiling: Sleep

## Slide 23: Backend

## Slide 24: Goal
Receive sensor data from Frost Detector (OCTA)
Make sensor data available to the mobile app
Send a push notification on a new reading
User system to segregate multiple Frost Detector systems

## Slide 25: Problems
User system isn’t implemented fully
   As a proof of concept, this feature isn’t required

## Slide 26: Achieved
The Frost Detector Service
  Listens to new readings on an MQTT topic from the TTN cloud
  Decodes and maps the incomming data
  Stores new readings in an SQLite3 database
  Sends a push notification via FCM on a new reading
API
  HTTP GET (readings)
  HTTP POST (user token)

## Slide 27: Frontend - App

## Slide 28: Goal
Display readings history
Set the alarm time of the Frost Detector over BLE
Alert the user about the condition of its car windshield at the set alarm time
Predict frost or vapor on the windshield based on interior and exterior sensor readings

## Slide 29: Problems
The prediction of frost or vapor on a windshield
   We need 2 OCTAs for this to work
   Time constraint + redundant work

## Slide 30: Achieved
Notes: NUS = Nordic UART service